Setup Phase
Load Preparation
Load Configurations
Set options
Load stop sign from file and convert it to fences
Load global planner waypoints
Initialize controller:
LONGITUDINAL CONTROLLER - PID Control
LATERAL CONTROLLER - Stanley Method
        kp = 0.50
        ki = 0.30
        integrator_min = 0.0
        integrator_max = 10.0
        kd = 0.13
        kp_heading = 8.00
        k_speed_crosstrack = 0.00
        cross_track_deadband = 0.01
        x_prev = 0.0
        y_prev = 0.0
        yaw_prev = 0.0
        v_prev = 0.0
        t_prev = 0.0
        v_error = 0.0
        v_error_prev = 0.0
        v_error_integral = 0.0

Gather current data from the Carla server and compute the average timestep based on several initial iterations: gather data and send control command
Calculate the total episode frames: 1. for live plotter
2. set limitation for main process

Store pose history starting from the start position

Object Detection
Get camera images for object detection
Calculate the parkedcar bbox points base on detection

Live Plotter
Vehicle trajectory and control live plotting setup
update live plotter with loaded info and object detection result

Local planner setup
behavioural planner setup

Scenario Execution Loop
Iterate the frames until the end of the waypoints is reached or the total episode frames is reached. The controller simulation then ouptuts the results to the controller output directory.

Initialize the current timestamp

for frame in range(total episode frames):
Gather current data from the CARLA server
Update pose and timestamp
Wait for some initial time before starting the demo
Store collision history
Local Planner Update:
(This will use the collision_checker.py, velocity_planner.py, behavioural_planner.py and local_planner.py)
Compute open loop speed estimate.
Computes an open loop speed estimate based on the previously planned trajectory, and the timestep since the last planning cycle.

Calculate the goal state set in the local frame for the local planner.
bahavior_planner
Set lookahead based on current speed.
Perform a state transition in the behavioural planner.
Check to see if we need to follow the lead vehicle.
If yes:
Compute the velocity profile for the path, and compute the waypoints.
Use the lead vehicle to inform the velocity profile's dynamic obstacle handling.
(In this scenario, the only dynamic obstacle is the lead vehicle at index 1.)
If no:
local_planner
Compute the goal state set from the behavioural planner's computed goal state.
Calculate planned paths in the local frame.
Transform those paths back to the global frame.
collision_checker
Perform collision checking.
Compute the best local path.
If no path was feasible, continue to follow the previous best path.

Update the controller values and controls
Update the live plotter

Output controller command to CARLA server
If the end of demo:
Stop vehicle and Store outputs to the controller output directory.